## Slide 1: SCRAP: Architecture for Signature-Based Protection from Code Reuse Attacks
Mehmet Kayaalp, Timothy Schmitt, Junaid Nomani, Dmitry Ponomarev and Nael Abu-Ghazaleh
Department of Computer Science
State University of New York at Binghamton
Presented at the19th IEEE International Symposium on High-Performance Computer Architecture (HPCA-19), February 25th, 2013

## Slide 2: Vulnerability Classification from NIST-NVD
*01/2010 – 12/2012 CVE Records (Severity 7 – 10)
Chart: 
| Buffer Errors | SQL Injection | Resource Management Errors | Input Validation | Code Injection | Permissions, Privileges, and Access Control | Numeric Errors | Other
 | 1378 | 849 | 478 | 392 | 351 | 293 | 216 | 674

## Slide 3: Buffer Overflow and Code Injection Attack: Example
main (int argc, char **argv)
{
...
vulnerable(argv[1]);
...
}
vulnerable(char *str1)
{
char str2[100];
strcpy(str2,str1);
return;
}
0x0000
0xFFFF
Stack growth
Stack frame for main()
Stack frame for vulnerable()
return address
str2
malicious input
(str2)
xor ecx, ecx
mul ecx
lea ebx, [esp+8]
mov al, 11
int 0x80
malicious return

## Slide 4: Existing Protection from Code Injection Attacks: No Execute Bit (NX)
0x0000
0xFFFF
WRITABLE
NOT EXECUTABLE
xor ecx, ecx
mul ecx
lea ebx, [esp+8]
mov al, 11
int 0x80
malicious return
Mark memory pages as
  Either WRITABLE
  Or EXECUTABLE
  But not both
Standard technique in current processors and operating systems
  Intel XD bit
  AMD XN bit
  Windows DEP
  Linux PaX
Stack growth

## Slide 5: Next Frontier: Code Reuse Attacks (CRAs)
Key Idea: Reuse existing library code instead of code injection
Bypass NX
Return Oriented Programming
Jump Oriented Programming

## Slide 6: Return Oriented Programming Attacks
Turing-complete
  X86
  SPARC
  ARM
Exploits
  Voting machine
  Atmel sensor
  Cisco router
  Xen hypervisor
  Jailbreak
  Pwn2Own
Automated tools
Microsoft BlueHat Prize ($260K)

## Slide 7: Return Oriented Programming (ROP)
0x0000
0xFFFF
Stack growth
Stack frame for main()
Stack frame for vulnerable()
<B>
<D>
<C>
xor ecx, ecx
mul ecx
lea ebx, [esp+8] mov al, 11
int 0x80
malicious return
xor ecx, ecx
ret
lea ebx, [esp+8]
ret
mov al, 11
int 0x80
mul ecx
ret
<A>
<Address A>
<Address B>
Page marked as EXECUTABLE
<Address C>
<Address D>

## Slide 8: Jump Oriented Programming
0x0000
0xFFFF
Stack growth
Stack frame for main()
Stack frame for vulnerable()
xor ecx, ecx
mul ecx
lea ebx, [esp+8] mov al, 11
int 0x80
malicious return
pop edi
jmp edi
lea ebx, [esp+8]
jmp esi
mov al, 11
int 0x80
mul ecx
jmp esi
<register values>
<C>
<D>
<F>
<E>
<B>
xor ecx, ecx
jmp esi
popa
jmp esi
<Address A>
<Address B>
<Address C>
<Address D>
Page marked as EXECUTABLE
<Address E>
<Address F>
Dispatcher Gadget

## Slide 9: Defending Against JOP Attacks
Use solutions preventing buffer overflows
  Bounds Checking
  Information Flow Tracking
Ensure the legitimacy of jump targets at runtime
  {Abadi-05}: Control-Flow Integrity (USENIX Security)
  {Kayaalp-12}: Branch Regulation (ISCA)
Signature-based detection
  Detect the anomaly in control flow

## Slide 10: Prior Work on Signature-Based Detection
“DROP: Detecting ROP malicious code”
  P. Chen et al. ICISS 2009
    if (# instructions between returns <= 5) then it is a gadget
    if (# consecutive gadgets >= 3) then it is a ROP attack

## Slide 11: DROP
Gadget Length
max tolerable gadget length for CRA
min # gadgets to launch a CRA
Consecutive Gadgets
Regular workloads
CRAs
N=5
S=3

## Slide 12: Building on DROP
Apply the same idea to
  Indirect jumps
  Indirect calls
Adjust the thresholds

## Slide 13: Extending DROP for JOP
max tolerable gadget length for CRA
min # gadgets to launch a CRA
Regular workloads
CRAs
Indirect jumps/calls are not that frequent
Added dispatcher gadgets

## Slide 14: Case of Long Gadgets
Side effects
  Overwrite registers/memory locations
  May cause exceptions
    adc [ebx-0x74EBDBAC], cl
  Limited number of registers
    One for the dispatcher
    One for jumping back to the dispatcher
    Only 6 left (in x86)

## Slide 15: Gadget Length and State Changes
Chart: Gadget Length
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
State Changes ≤ 2 | 0.29907 | 0.1759 | 0.065362 | 0.01856 | 0.0043804 | 0.00095317 | 0.00019972 | 7.0053e-05 | 0 | 0
State Changes ≤ 1 | 0.19815 | 0.05724 | 0.014821 | 0.0026987 | 0.00042004 | 6.3545e-05 | 0 | 0 | 0 | 0

## Slide 16: Defeating DROP
Make the attack pattern less predictable
  Perform some unnecessary computation
  Without harming attack state
Call a function
  Execute many instructions
  Return to the same point in the attack
  Caller saved registers stay intact
    ebx, esi, edi, esp, ebp

## Slide 17: Delay Gadgets
call [ecx-0x56000a00]
add bl, bh
inc ebx
add dh, bh
jmp edi
Dispatcher
Gadget
Functional
Gadget
Delay
Gadget
add [ebx], edx
jmp esi
pop eax
jmp eax
atoi()

## Slide 18: Summary of DROP Limitations
Implemented in software
  5x slowdown
Tight margin for detecting ROP
  False positives/negatives
Easily defeated by using delay gadgets

## Slide 19: Our Proposal: SCRAP
Signature-Based CRA Protection
Detects CRAs with delay gadgets
No false positives for regular workloads
Implemented in hardware
  Low overhead
  Protects legacy binaries

## Slide 20: Attack Signatures
Symbol | Instruction
w | Indirect Jump
x | Indirect Call
y | Call
z | Return
a | All Other
DROP-like Signature Definition:
Up to N instructions
S or more gadgets

## Slide 21: SCRAP Attack Signatures
Symbol | Instruction
w | Indirect Jump
x | Indirect Call
y | Call
z | Return
a | All Other
Signatures with delay gadgets (N=5, S=3):
Attack has 3 parts
Each part has a Gadget and Delays
A Gadget has up to 5 instructions
Delay is a function call
A function call can be a Delay as long as it is not an Attack itself

## Slide 22: Example Signatures
Signature | Detected by DROP-like? | Detected by SCRAP?
aaawaawaaw
awaaxaaaaw
awaxaaaaaazaxaw
awaxaayaazaaaazaxaw
✔ | ✔
✘ | ✔
✔ | ✔
✘ | ✔

## Slide 23: Pushdown Automata

## Slide 24: Simple Implementation
Augment the stack of PDA with Secure Call Stack
  Save the PDA state for calls
  Restore for returns
  Modify for indirect jumps
Commit throttling
  Only one stack operation for a commit window
  Negligible slowdown
  Simplifies the circuitry

## Slide 25: SCRAP Hardware

## Slide 26: False Positives for SCRAP
CRAs
Gadget Length
Consecutive Gadgets
5
6
7
8
9
10
11
12
13
1
2
3
4
5
6
SPEC 2006 benchmarks
140 Shell-storm CRA exploits

## Slide 27: Performance of SCRAP

## Slide 28: Conclusions
Signature-based detection of CRAs is promising
  No source code, simple, low-overhead, effective
Naïve approaches can be defeated
  Delay gadgets
We presented SCRAP
  Simple hardware state machine,
  Protects unmodified legacy binaries,
  No changes to software layers,
  Small slowdown: 1% on average
  No false positives

## Slide 29
Thank you! Questions?

## Slide 30: Backup Slides

## Slide 31: Unintended Instructions
08048484: E8 33 FE FF FF
08048489: 8D BB 18 FF FF FF
0804848F: 8D 83 18 FF FF FF
08048495: 29 C7
08048488: FF 8D BB 18 FF FF
0804848E: FF 8D 83 18 FF FF
08048494: FF 29
Code Snippet from __libc_csu_init function
08048484: E8 33 FE FF FF
08048489: 8D BB 18 FF FF FF
0804848F: 8D 83 18 FF FF FF
08048495: 29 C7
Unintended Code Snippet from __libc_csu_init function
call <_init>
lea edi, [ebx-e8h]
lea eax, [ebx-e8h]
sub, edi, eax
dec [ebp-e745h]
dec [ebp-e77dh]
jmp [ecx]
FF
8D BB 18 FF FF
FF
8D 83 18 FF FF
FF
29

## Slide 32: Gadget Length
Long gadget means more intermediate instructions
Chart: Gadget Length
| 1 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
 | 0.30361 | 0.4747 | 0.56867 | 0.64819 | 0.68916 | 0.71807 | 0.73494 | 0.75663 | 0.7759 | 0.78554 | 0.79759 | 0.80482 | 0.81928 | 0.83133 | 0.84096 | 0.8506 | 0.85301 | 0.86265 | 0.86988 | 0.87711 | 0.88434 | 0.89157 | 0.89398 | 0.89639 | 0.9012 | 0.91325 | 0.92048 | 0.9253 | 0.93253 | 0.93494 | 0.93735 | 0.93976 | 0.94217 | 0.94458 | 0.95181 | 0.95422 | 0.95904 | 0.96386 | 0.96627 | 0.97108 | 0.97831 | 0.98795 | 0.99277 | 0.99277 | 0.99518 | 0.99518 | 1 | 1 | 1 | 1

## Slide 33: Two threshold SCRAP